## Slide 1: Stability and Control
Non-Dimensional Derivatives
Part 1
Greg Marien
Lecturer

## Slide 2: Introduction
Complete Aircraft wing, tail and propulsion configuration, Mass Properties, including MOIs
Use results to determine stability (Etkin)
Non-Dimensional Derivatives (Roskam)
Dimensional Derivatives (Etkin)
Calculate System Matrix [A] and eigenvalues and eigenvectors
Reading:
Nicolai - CH 21, 22 & 23 Roskam – VI, CH 8 & 10
Other references:
MIL-STD-1797/MIL-F-8785 Flying Qualities of Piloted Aircraft
Airplane Flight Dynamics Part I (Roskam)
LOFT needs to be complete

## Slide 3: What are the requirements?
Entry criteria (but don’t wait to set up your spreadsheet/code)
  Loft geometry complete
  Drag Polar for flight condition
Preliminary Aero Analysis may be complete, if not, you will do it here.
  Lift vs alpha curves for ALL surfaces for flight condition
  Lift Curve vs. alpha for entire aircraft for flight condition
Flight Condition given:
  Airspeed: M = ?
  Altitude: ? ft.
  Standard atmosphere
  Configuration: ?
  Fuel: ?%
Assume all Derivatives are 0 for this analysis
CLa from now on is the Lift Slope for the entire aircraft, i.e. wing, body, horizontal stab, canard, etc.
Evaluate your aircraft for meeting the stability requirements
See SRD for values

## Slide 4: Control Axis Review
(Nicolai)
Notes: Important points- keep these handy and commit to memory:
Direction of Positive Forces, note same direction as ACS axis
Stability Control Axis flipped from ACS
Direction of Positive Moments – RH Rule based on Stability Control Axis
CG, Wing a.c. and Aircraft Neutral Point
Derivatives: Note the sampling on the chart… but there is many more!
Derivative is exactly what it sounds like: find the rate of change (slope) of something based as a function of another, i.e. rate of change of lift based on AoA.
Methodology comes from years of research and is documented in DATCOM, but is presented in multiple sources, i.e. Roskam, Nicolai, etc.

## Slide 5: Steady State Coefficients of Flight Condition
Coeff. |  | Ref/Eq | Expectation in Report
CD1 | Calculated from drag polar | R VI, Sec 10.1 | Show on drag polar curve
CL1 | Calculated | R VI, Sec 10.1 | Show on lift curve
CM1 | Calculated or from CM vs CL Curve | R VI, Sec 10.1 | Show on CM vs CL curve
CTx1 | = CD1 for steady state conditions | R VI, Sec 10.1 | State value
CMT1 | Takes into account engine placement | R VI, Sec 10.1 | Show side view of aircraft and input dimensions for calculation
Straight forward from your current knowledge.
Subscript “1” signifies the flight condition being analyzed
See SRD for flight condition

## Slide 6: Getting your flight condition values…
Curves need to be developed if you have not done it.
Curves have to be for the flight condition M.
Notes: As my wife would say…. GET ON IT!

## Slide 7: Speed Derivatives
Coeff. |  | Ref/Eq | Expectation in Report
CDu or CXu | Drag due to speed | R VI Eq 10.10 | Show figure, with area being analyzed
CLu or CZu | Lift due to speed | R VI Eq 10.11 | Show figure, with area being analyzed
CMu | Moment due to speed | R VI Eq 10.12 | Show all work
CTxu | Thrust due to speed (not used for this analysis) | R VI Eq 10.15 | N/A
CMTu | Thrust Moment due to Speed (not used for this analysis) | R VI Eq 10.16 | N/A
Thrust vs. Speed Coefficients - assume zero for this analysis
Notes: Change in something based on the change of aircraft speed….
Q. How does the lift coefficient change with speed change? What is lift coefficient a function of?

## Slide 8: CDu Drag due to Speed
R VI, Eq 10.10
R VI. Fig 10.3
No sample calculations required, show figure, drag polars that define the curve and document values
Note: This is from the drag polar, not CDo
CAS/APT
SSBJ

## Slide 9: CLu Lift due to Speed
Subsonic and Supersonic: R VI, Eq 10.11
Transonic: Fair curves from M = 0.8 to 1.2
R VI. Fig 10.4
No sample calculations required, show figure and document values

## Slide 10: Cmu Pitching Moment due to Speed
R VI, Eq 10.12
Determine , R VI. Eq 8.82 (Too much to discuss in this class, just dive in and work the problem.)
See me if you get stuck.
Once is determined, find the for
Slope is plotted for vs. M
Show all work

## Slide 11: AoA Derivatives
Coeff. |  | Ref/Eq | Expectation in Report
CDa | Drag due to AoA | R VI Eq 10.17 | See chart
CLa | Lift due to AoA | R VI Eq 8.42 | See chart
CMa | Pitching Moment due to AoA | R VI Eq 10.19 | See chart
Thrust vs. AoA- assume zero for this analysis

## Slide 12: CDa Drag due to AoA
R VI, Eq 10.17
R VI. Fig 10.5
No sample calculations required, show figure and document values

## Slide 13: CLa Lift due to AoA
R VI, Eq 8.42
Show all work, include all downwash/upwash gradient
graphs with values and your R VI, Fig 8.66 for your aircraft
All lift curves determined for flight condition M (Too much to discuss in this class, just dive in and work the problem.)
See me if you get stuck.

## Slide 14: Cma Pitching moment due to AoA
R VI, Eq 10.19
No sample calculations required, show CM/CL figure and document values
Should have Cm/CL graph or values calculated, if not you need to do this.
Should have all values, plug and chug!

## Slide 15: AoA Rate Derivatives
Coeff. |  | Ref/Eq | Expectation in Report
CDἀ | Drag due to rate of AoA | R VI Eq 10.21 (negligible if subsonic) | For SSBJ, see DATCOM
CLἀ | Lift due to rate of AoA | R VI Eq 10.22 | 
CMἀ | Pitching Moment due to rate of AoA | R VI Eq 10.24 | 

## Slide 16: CLἀ Lift due to rate of AoA
R VI, Eq 10.22
Horizontal or lift slope
Dynamic Pressure “Fudge Factor” due to kinetic energy changes due to wing body drag or propeller slip stream interaction
R VI, Eq 8.36, 8.37 and Fig 8.63
Horizontal Volume Ratio
Downwash Factor, R VI Eq 8.45
Show all work, including your version of R VI, Fig 8.63
Only need to show downwash factor calculation once

## Slide 17: Cmἀ Pitching Moment due to rate of AoA
R VI, Eq 10.24
Horizontal or lift slope
Dynamic Pressure “Fudge Factor” due to kinetic energy changes due to wing body drag or propeller slip stream interaction
R VI, Eq 8.36, 8.37 and Fig 8.63
Horizontal Volume Ratio
Downwash Factor, R VI Eq 8.45
R VI Fig 10.6
R VI. Fig 10.6
No sample calculations required, show figure and document values